## Slide 1: Occupational specialism: Low Carbon Engineering PowerPoint K1.8 / K1.9: Relationship Management and Communication & Stakeholder Management

## Slide 2
Introduction / Starter
Warm-up
What’s the quickest way a heat pump job goes wrong without anyone touching the installation?
Think–pair–share
List 3 examples of non-technical failures:
Wrong expectations
Poor handover
Unclear scope
Share back
Discussion points:
• Which example causes the biggest cost or risk?
• Why?
Notes: Tutor prompt: steer toward communication, scope, competence boundaries, documentation.

## Slide 3: Objectives (K1.8 + K1.9)
Competence & Limits
Recognise limits of competence and what not to do.
Specialist Engagement
Know when to engage competent trades and specialists.
Effective Communication
Use effective communication for different audiences.
Stakeholder Management
Manage expectations and impacts on essential services.
Key Outputs
Produce outputs: quote → invoice → handover docs.
Notes: Note: K1.9 is the larger focus; K1.8 is a concise refresher.

## Slide 4: K1.8 Limits of competence: what not to do
Critical Prohibitions
No Unauthorised Work: Do not carry out regulated work outside certification/authorisation.
No Refrigerant Handling: Do not open/break sealed refrigerant circuits (refer F-Gas certified).
No False Verification: Do not sign off work you cannot verify or are not authorised to sign.
No Overrides: Do not override manufacturer instructions or safety devices.
Golden Rule
Do not guess: stop, check, escalate
Notes: Examples:
- Refrigerant circuit work (K1.5)
- Unvented cylinder / electrical sign-off where required
Image source (choose and log):
https://www.freepik.com/search?query=stop%20sign%20safety&type=vector

## Slide 5: K1.8 When to engage competent trades/specialists
Electrician
Supply alterations, testing and certification.
Example: New dedicated circuit for GSHP/ASHP, upgraded protection.
Gas Safe / OFTEC
Combustion appliances or fuel systems.
Example: Mains gas boiler commissioning or oil fuel line work.
F-Gas Engineer
Refrigerant handling, recovery, leak repair.
Example: Repairing a sealed refrigerant circuit on a HP.
Scheme Installer/Designer
Certification evidence or design sign-off.
Example: Design evidence and commissioning records for audit.
Other Expertise
Structural, planning, water hygiene/quality.
Example: Outdoor unit fixings or DHW hygiene strategy.
Notes: Quick rule for learners:
Electrical changes beyond simple connection/config → electrician
Combustion appliances/fuel systems → Gas Safe / OFTEC
Refrigerant circuit work → F-Gas
Audit/assurance evidence + sign-off → scheme designer/installer
Ask learners: “What would you record before referring?”
Fault codes, symptoms, readings observed, what checks you completed, photos (if permitted), and what you did not do (e.g. did not open refrigerant circuit).
Stop point idea: Wordwall/Quizizz “Who do you refer to?” (created separately).

## Slide 6: K1.8 Limits of competence: When to engage competent trades/specialists
Scenario A: Mains gas heating system work
Altering/commissioning boiler, flue, or gas pipework
→ Gas Safe
Scenario B: Installing an oil boiler or fuel system
Oil appliance commissioning or fuel supply changes
→ OFTEC
Scenario C: Installing a GSHP (Electrical)
Fixed wiring/protection upgrades/testing/certification
→ Electrician
Scenario D: Repairing sealed refrigerant system
Refrigerant handling/recovery/leak repair/circuit opening
→ F-Gas
Scenario E: Customer requires scheme evidence/sign-off
If scheme requires validated design/commissioning evidence
→ Scheme installer/designer
Notes: Electrical changes beyond simple connection/config → electrician
Combustion appliances/fuel systems → Gas Safe / OFTEC
Refrigerant circuit work → F-Gas
Audit/assurance evidence + sign-off → scheme designer/installer
Ask learners: “What would you record before referring?”
Fault codes, symptoms, readings observed, what checks you completed, photos (if permitted), and what you did not do (e.g. did not open refrigerant circuit).

## Slide 7: K1.8 Escalation: what to record and hand over
Record Symptoms
What the system is doing or not doing.
Fault Codes & Alarms
Capture alarms and current operating conditions.
Checks Completed
List all checks within competence (no refrigerant disturbance).
Actions Taken & Outcomes
Detailed log of steps taken and the resulting system state.
Clear Handover
Ensure technical handover to improve first-time fix probability.
Notes: Workbook task: Handover note template (created by others).

## Slide 8: K1.9 Effective communication: principles
Clear Structure
What / Why / Impact / Next Action.
Accurate
Evidence-based, not assumptions.
Audience-Matched
Technical vs. non-technical language.
Timely
Communicate early to avoid surprises.
Confirm Understanding
Teach-back / closed-loop communication.
Notes: Image source (choose and log):
https://www.freepik.com/search?query=communication%20icons&type=vector

## Slide 9
Methods and styles (what to use when)
Communication Methods
Face-to-face
Phone
Email / Text
Drawings / Photos
Demonstrations
Communication Styles
Informative: Facts & next steps (updates, instructions)
Persuasive: Recommendations with evidence
Empathetic: Acknowledge concerns (cost, disruption)
Assertive: Safety-critical boundaries (stop work)
Consider the Audience
Tailor approach for:
Customers
Contractors
Inspectors
Colleagues
Assess the Situation
Differentiate between a routine update and an urgent safety issue to determine the appropriate method and style.
Notes: Learner message: you will often switch style in one conversation.
“Assertive” ≠ rude — it’s calm, clear, and safety-led.
Stop point: ask learners to give one situation where each style is most appropriate (2 mins).

## Slide 10
Methods and styles (what to use when)
Scenario message: “We need to isolate power and heating for 2 hours to complete the work safely.”
Informative
Focus on facts and timeline. Provide clear, objective details about the process.
KEY ELEMENTS:
Facts
Timeline
Persuasive
Explain why it benefits them. Use logic to build agreement.
KEY ELEMENTS:
Benefit-driven
Logical reasoning
Empathetic
Acknowledge the impact of the message. Show understanding of their situation.
KEY ELEMENTS:
Acknowledge impact
Active listening
Assertive
Establish safety boundaries. Clear, firm, and non-negotiable on safety.
KEY ELEMENTS:
Safety boundary
Firm communication
Deliver this message in 4 ways based on the communication style required by the situation.
Notes: Informative: “To complete the installation safely we’ll isolate power and heating from 10:00 to 12:00. I’ll confirm everything is restored before I leave.”
Persuasive: “If we isolate for 2 hours now, we can complete the work correctly and avoid repeat visits or faults later. It protects the system and your warranty.”
Empathetic: “I know losing heating and power is inconvenient, especially today. We’ll keep the downtime as short as possible and I’ll keep you updated throughout.”
Assertive (safety): “I can’t continue unless the system is isolated. It’s a safety requirement. Once it’s isolated, we can proceed safely.”
Stop point options
Role-play pairs (5 mins): one learner is the installer, one is the customer. Swap roles.
Wordwall/Quizizz placeholder: “Which style is best?” (created separately).

## Slide 11: Technical vs. non-technical vocabulary
Translate technical terms into plain English
Aim: Help stakeholders understand decisions.
Focus: Outcomes and meaning (what it does, why it matters).
Example: "weather compensation" → "automatically adjusts water temp based on outdoor air to save energy."
Use technical terms with engineers
Aim: Accurate diagnosis and safe handover.
Action: Use precise terms (ΔT, head/flow, fault codes).
Example: "flow temp 40°C, return 34°C, ΔT 6°C, pump on constant speed."
Avoid misleading simplifications
Don't oversimplify to the point of inaccuracy. Explain key trade-offs (e.g. comfort vs. efficiency).
Confirm understanding (Teach-back)
Don't assume understanding—check it. Ask the customer to repeat the key action in their own words.
Example Teach-back Questions:
"Can you show me how you would boost hot water if you needed it?"
"What will you do if you see this fault message?"
"What temperature do you normally leave the thermostat at?"
Notes: Examples to translate: weather compensation, defrost cycle, flow temperature.
Stop point: Wordwall/Quizizz 'Translate the jargon' (developed separately).

## Slide 12
Stakeholders: expectations and interrelationships
Customer / occupant
Cares about: comfort, running costs, hot water, noise, minimal disruption.
Needs: clear explanations of system feel, simple controls guidance, handover pack.
Link: Feedback affects performance.
Employer / Contractor
Cares about: scope, timeline, quality, profitability, and safe working.
Needs: accurate updates, risk controls (RAMS), organised evidence pack.
Link: Communication prevents disputes.
Building Control
Cares about: compliance evidence and correct system documentation.
Needs: commissioning records, handover docs, compliance confirmation.
Link: Affects sign-off & confidence.
DNO / Utilities
Cares about: safe, reliable supply and electrical demand within site limits.
Needs: early ID of constraints, upgrade confirmation, network coordination.
Link: Delays here shift install dates and impact communication.
Neighbour / Community
Cares about: noise, visual impact, working hours, and physical disruption.
Needs: considerate siting, proactive communication, noise-aware choices.
Link: Concerns trigger planning issues and reputational risk.
Notes: Quick learner check: “For each stakeholder, what’s the one thing that would cause a complaint or delay?” This helps them understand why stakeholder management matters as much as technical work.

## Slide 13: Collaborative working (design & delivery)
Agree roles and responsibilities early
Confirm who is responsible for: design, electrical, pipework, and sign-offs. Avoids gaps where tasks are assumed to be someone else's responsibility.
Coordinate sequencing with other trades
Plan work order so trades don't block each other. Proper sequencing reduces downtime, repeat visits, and costly rework.
Share constraints early
Confirm access, noise sensitive positions (ASHP), and working hours. Agree isolation windows for essential services to minimise disruption.
Use evidence to justify decisions
Base choices on facts: heat loss results, emitter suitability, and site constraints. Protects the installer and explains choices to customers.
Manage change professionally
If site conditions differ from assumptions, pause and agree a variation:
Confirm what changes, why, cost/time impact, and who approves.
Update drawings/job file and confirm the new plan before continuing.
Notes: Give learners a mini case: “Outdoor unit location changed due to noise/boundary issue.” Ask them to list:
who must be told (customer, contractor, neighbour if affected, electrician, scheme)
what evidence supports the change (planning/noise constraint, access, airflow/clearances)
what must be updated (scope, cost, programme, records).
Workbook task: roles & responsibilities table (created by others).

## Slide 14
Ethical communication (benefits, costs, drawbacks)
Be honest about benefits
Realistic Terms: Steady comfort, lower emissions, and potential savings when system is correctly sized/set up.
Avoid absolute promises without evidence.
Be honest about drawbacks
Considerations: Upfront cost, space requirements, noise, and longer run times.
Habit Change: Steady temps vs. "blast heat" and DHW recovery times.
Explain assumptions clearly
Factors: Insulation, heat loss, radiator sizes, and flow temperatures.
Communicate early: if assumptions are wrong, performance and cost will change.
Avoid overselling
Recommend what fits the customer and property, not what is easiest to sell.
Explain necessary upgrades (insulation, electrical) openly.
Document what was agreed
Record the chosen design, key settings, exclusions, and any compromises made.
Good documentation protects the customer, business, and engineer.
Notes: Scenario: customer wants “boiler-like heat” and insists on high flow temperatures. Ask learners:
What are the ethical risks of agreeing without explaining the consequences?
What wording would you use to explain the trade-off (comfort vs. efficiency vs. cost)?
What must be documented in the job file/quote?

## Slide 15: Protecting essential services (minimise disruption)
Services affected: electricity, water, heating/hot water, telecoms.
Plan isolation: when, how long, and customer needs.
Temporary services: plan ahead where required.
Sequence work to reduce downtime (prepare first, isolate last).
Communicate before/during/after and confirm restoration.
Notes: Stop point: Wordwall/Quizizz 'Which service is impacted?' (developed separately).

## Slide 16: Scenario activity (15 mins): essential services plan
Scenario: customer works from home and relies on broadband + hot water daily.
Task: create a disruption-minimisation plan for install/commission day.
Include: isolation window, temporary measures, communication plan.
Output: 6-bullet 'Customer Disruption Plan’ & what you will document.
Notes: Workbook task: Customer Disruption Plan template (created by others).

## Slide 17: Outputs: estimate vs. quotation
Estimate (indicative price)
Best-guess cost based on limited info.
Can change with site conditions or scope.
Use: Early enquiry, pre-survey.
Quotation (fixed offer)
Priced offer for defined scope.
States validity, terms, and assumptions.
Use: After survey/design decisions.
Minimum Good Practice (Both)
Scope: Deliverables & components. In/Exclusions: Explicit boundaries. Assumptions: Conditions relied on. Timescales: Lead times & duration.
Variations / Change Control
Stop and agree changes in writing if scope shifts—protects both parties.
Notes: Tutor note: keep practical, not legal advice.
Example estimate wording: “Estimated £X–£Y subject to survey and final design.”
Example quote wording: “Quoted £X for defined scope. Variations only by written agreement.”
Key learner takeaway: clarity + written variation control prevents most complaints.

## Slide 18: Outputs: invoice (what good looks like)
Matches agreed quote/scope
The invoice should reflect the original quotation plus any approved variations.
Extra work must be clearly listed as a variation with customer approval referenced.
Clear line items & dates
Break costs down into understandable items (e.g. "ASHP installation", "commissioning").
Include key dates: survey, installation, commissioning, and completion.
References evidence/completion
Reference documents like commissioning records, handover packs, or photos.
Note if certifications (e.g. electrical, Building Control) are provided or pending.
Tone & Payment Terms
Use polite, factual language. State due dates, methods, and staged payments clearly.
Provide contact details for queries to reduce conflict and speed up resolution.
Key Outcome: Professionalism at the point of invoice builds trust and ensures faster payment.
Notes: A “strong invoice” allows the customer to answer:
What did you do?
When did you do it?
What was included?
What changed and who agreed it?
What documents prove completion?

## Slide 19: Outputs: performance + compliance + handover (1 of 2)
Performance document
(what the customer should expect)
Clear summary of intended operation: design intent, heat loss/emitter assumptions, and "normal" behavior (defrost, DHW recovery).
Manages expectations by explaining how low temp heating differs from a boiler.
Compliance certificate
(proof the correct route was followed)
Evidence of met compliance routes (e.g. self-certification via competent person scheme).
Confirms installation meets standards and protects the customer and business.
Notes: Link forward: K1.41 covers commissioning documentation in depth.
A good handover means the customer can answer:
How do I use it day-to-day?
What’s normal vs. a fault?
What settings should I avoid changing?
What maintenance is needed and when?
Who do I contact if there’s an issue?
Stop point: Wordwall match 'document → purpose' (developed separately).

## Slide 20: Outputs: performance + compliance + handover (2 of 2)
Handover documents
(what the user needs to run the system)
Complete pack: user guide, settings summary, warranty, and contact details.
Includes key records: commissioning summary and maintenance requirements.
Controls demonstration
(how to use it efficiently)
Demonstrate key actions: schedules, temp adjustments, DHW boost, alerts.
Confirm understanding via teach-back ("show me how") to avoid callbacks.
Key Outcome: Effective handover ensures customer satisfaction, compliance, and reduced maintenance callouts.
Notes: Link forward: K1.41 covers commissioning documentation in depth.
A good handover means the customer can answer:
How do I use it day-to-day?
What’s normal vs. a fault?
What settings should I avoid changing?
What maintenance is needed and when?
Who do I contact if there’s an issue?
Stop point: Wordwall match 'document → purpose' (developed separately).

## Slide 21: Demonstration of controls (handover skill)
Show the key everyday actions
How to change schedules, adjust temperature setpoints, use DHW boost, and set holiday mode.
Highlight "safe to change" vs. "left alone" settings.
Explain normal behaviours
Defrost cycles: Explain sights/sounds and that it's normal in cold weather.
Typical low-carbon behaviour: longer run times, steady heat, and slower swings.
Confirm using teach-back
Ask customer: "Show me how you'd boost hot water" or change a schedule.
Correct gently and repeat until they are confident.
Guidance & support details
Provide a "quick start" note: setpoints and problem troubleshooting.
Leave contact details, warranty info, and maintenance records.
Key Goal: Ensure the customer feels confident and competent to operate their new system efficiently.
Notes: A good controls handover reduces callbacks by preventing: constant overrides, high flow temp settings, incorrect schedules, and unnecessary service calls during normal defrost behaviour.
https://www.freepik.com/search?query=smart%20thermostat%20illustration&type=vector

## Slide 22: Recap checkpoint (5 mins)
1) List two examples of work you must refer to another trade.
2) Translate one term into plain English.
3) Name two stakeholders and what they need from you.
4) Name two ways to minimise disruption to essential services.
Stop point: Wordwall/Quizizz recap (developed separately)
Notes: Suggested answers (examples):
- Refer: refrigerant handling; electrical certification; unvented sign-off
- Translate: weather compensation = adjusts temperature with weather
- Stakeholders: customer (controls), contractor (scope/evidence)
- Minimise disruption: plan isolation; temporary services; communicate.
Workbook recap questions (created by others).

## Slide 23: Summary & questions
K1.8: know your limits, stop and refer appropriately.
K1.9: communicate clearly, ethically and to the right audience.
Minimise disruption and document decisions and evidence.
Any questions before moving on?
Notes: Add chosen video links here (notes only) and mirror in SoW:
- Video 1 (communication/customer expectations): [PASTE LINK]
- Video 2 (handover/controls demo): [PASTE LINK]
Artlog: paste image source URLs used.

## Slide 24
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.