## Slide 1
Occupational Specialism: Protection Systems Engineering
K1.2 Electrical and Electronic Principles
PowerPoint 1.2: Electrical and Electronic principles

## Slide 2: Introduction
This session covers basic principles of electrical and electronic science.
We'll explore the fundamental relationships between:
voltage, current, resistance, and power
examine circuit components like resistors, capacitors, and inductors
and delve into the properties of semiconductors and transformers.

## Slide 3: Objectives
By the end of this session, you should be able to:
Understand basic electrical and electronic science principles relevant to protection systems.
Be able to apply Ohm’s Law in protection systems.
Understand the behaviour of basic electrical and electronic components used in protection systems.

## Slide 4
Overview
Electrical fundamentals
Voltage, current, resistance, and power relationships
Circuit components
Resistors, capacitors, inductors, and transformers
Measurement techniques
Using digital multimeters and testing components
Semiconductor devices
Diodes, LEDs, and transistors

## Slide 5
Fundamental electrical quantities
Voltage (V)
The electrical pressure or potential difference that drives current through a circuit. Measured in volts (V), it represents the energy per unit charge available to move electrons through a conductor.
Current (I)
The flow rate of electric charge through a conductor. Measured in amperes (A), it quantifies how many electrons pass a specific point in a circuit per second.
Resistance (R)
The opposition to current flow in an electrical circuit. Measured in ohms (Ω), it determines how much current will flow for a given voltage.
Understanding these fundamental quantities is essential for analysing any electrical circuit. Their relationships form the foundation of electrical theory and are the basis for designing and troubleshooting fire and security systems.

## Slide 6
SI Units and Electrical Symbols
Quantity
Symbol
Unit
Unit Symbol
Voltage
V or E
Volt
V
Current
I
Ampere
A
Resistance
R
Ohm
Ω
Power
P
Watt
W
Capacitance
C
Farad
F
Inductance
L
Henry
H

## Slide 7
SI Units and Electrical Symbols
Standardised symbols and units are essential for clear communication in engineering documentation. When designing or maintaining fire and security systems, these symbols appear in schematics, datasheets, and technical manuals.
You need to recognise these symbols quickly to troubleshoot systems efficiently. Using them correctly means that specifications and measurements are understood consistently across different teams and organisations working on the same systems.

## Slide 8
Ohm's Law: The fundamental relationship
V = I × R
Voltage equals current multiplied by resistance.
If we know any two values, we can calculate the third.
I = V ÷ R
Current equals voltage divided by resistance.
Higher voltage or lower resistance increases current flow.
R = V ÷ I
Resistance equals voltage divided by current.
Used to determine the resistance needed to limit current to a specific value.
Notes: Shutterstock.com

## Slide 9
Ohm's Law: The fundamental relationship
Ohm's Law is the cornerstone of electrical circuit analysis.
By understanding this relationship, you can predict how changes in one variable will affect others, which is essential for designing circuits that operate within safe parameters in security systems.

## Slide 10
Voltage drop in dc circuits
Source voltage
The initial electrical potential available from the power source.
Component voltage drop
Each component consumes part of the available voltage.
End device voltage
The remaining voltage available at the end of the circuit.

## Slide 11
Voltage drop in dc circuits
Voltage drop is a critical consideration in fire and security systems, especially for devices located far from power sources.
Insufficient voltage can cause sensors and alarms to malfunction or fail completely. Circuit designs must account for wire resistance and component voltage drops to make reliable systems.
In long cable runs, voltage drop calculations ensure that devices at the end of the line receive adequate power to function correctly under all conditions, including emergency situations.

## Slide 12
Electrical power in DC circuits
P = V × I (Watts = Volts × Amperes)
Power equals voltage multiplied by current, measuring the rate at which energy is transferred in a circuit.
P = I² × R (Watts = Amperes² × Ohms)
Power can also be calculated from current and resistance, critical for heat dissipation calculations.
P = V² ÷ R (Watts = Volts² ÷ Ohms)
Alternative power calculation from voltage and resistance, useful when current measurement is impractical.

## Slide 13
Electrical power in DC circuits
Understanding power consumption is crucial for fire and security system design. It determines battery backup requirements, heat generation, and system endurance during power outages.
Efficient power management extends system reliability and reduces operational costs while ensuring continuous protection.

## Slide 14
Material properties: Conductors vs Insulators
Conductors
Materials with loosely bound outer electrons that can move freely through the atomic structure.
Insulators
Materials with tightly bound electrons that resist the flow of electrical current.
Copper: Excellent conductivity, widely used
Aluminium: Lighter weight, used in power lines
Gold: Superior corrosion resistance
Silver: Highest conductivity but expensive
Glass: High temperature resistance
Rubber: Flexible, used for cable jackets
Ceramics: Used in high-voltage applications
Plastics: Versatile and cost-effective

## Slide 15
Material properties: Conductors vs. Insulators
The correct selection of conductors and insulators is critical in fire detection and security systems. Conductors must maintain signal integrity while insulators prevent short circuits and electrical hazards, especially in environments with extreme temperatures or corrosive conditions.

## Slide 16
Series resistive circuits
Total resistance
RT = R1 + R2 + R3 + ...
Current flow
Current is identical through all resistors
Voltage division
Voltage drops proportional to resistance values

## Slide 17
Series resistive circuits
In series circuits, the same current flows through all components, but the voltage is divided among them proportionally to their resistance. This principle is crucial for voltage divider networks used in sensor interfaces and reference voltage generation in security systems.
When designing fire alarm circuits, understanding series resistance helps engineers calculate the voltage available to end-of-line devices and determine appropriate wire gauges for long cable runs to maintain system reliability.

## Slide 18
Parallel resistive circuits
Total resistance
1/RT = 1/R1 + 1/R2 + 1/R3 + ...
Current division
Current divides inversely proportional to resistance
Voltage distribution
Voltage is identical across all
resistors
Lower total resistance
Total resistance is always less than the smallest resistor

## Slide 19
Parallel resistive circuits
Parallel circuits are fundamental to many security system designs where multiple sensors or detectors must operate independently while connected to a common power source. The voltage remains consistent across all branches, ensuring reliable operation of all connected devices.
This configuration also provides redundancy - if one branch fails, the others can continue functioning, a critical feature for life safety systems.

## Slide 20
Parallel resistive circuits
Parallel circuit – Total resistance calculation
In a parallel circuit, the total resistance decreases as more resistors are added. The formula is:
Step-by-step guide
Step 1: Write the reciprocal formula
If you have three resistors:

## Slide 21
Parallel resistive circuits
Step 2: Find a common denominator
The least common denominator of 6, 3, and 2 is 6.
Convert each fraction:
Now add:

## Slide 22
Parallel resistive circuits
Step 3: Invert the result
Since:
Then:

## Slide 23
Combined series - parallel circuits
Identify pure series and parallel sections
Break down the complex circuit into recognizable patterns of purely series or parallel components.
Calculate equivalent resistances
Solve each section using appropriate series or parallel formulas, working from the innermost groups outward.
Determine total circuit behaviour
Calculate overall resistance, current flow, and voltage distribution throughout the simplified circuit.

## Slide 24
Combined series - parallel circuits
Series-parallel combinations are common in practical fire and security systems, allowing designers to create precise voltage dividers, current limiters, and specialized sensing circuits. Understanding how to analyze these networks is essential for troubleshooting complex systems when voltage or current measurements don't match expected values.
This analytical approach helps isolate faults and optimise circuit performance for maximum reliability in critical safety applications.

## Slide 25
Example: Resistor circuit calculations
Series resistor example
Three resistors of 470Ω, 1kΩ, and 2.2kΩ are connected in series across a 12V supply.
Find the total resistance and current flow.
Rtotal = 470Ω + 1000Ω + 2200Ω = 3670Ω
I = V/R = 12V/3670Ω = 3.27mA
Parallel resistor example
Two 10kΩ resistors are connected in parallel.
Calculate the total resistance.
Rtotal = (R₁ × R₂)/(R₁ + R₂) = (10kΩ × 10kΩ)/(10kΩ + 10kΩ) = 100kΩ/20kΩ = 5kΩ
EOL resistor application
A fire alarm circuit uses a 4.7kΩ end-of-line resistor. If a detector with 100Ω internal resistance activates, calculate the new circuit resistance.
The detector effectively places 100Ω in parallel with 4.7kΩ:
Rnew = (100Ω × 4700Ω)/(100Ω + 4700Ω) = 97.9Ω

## Slide 26
Example problems: Ohm's Law
Problem 1: Finding current
A smoke detector operating at 24V DC has an internal resistance of 600Ω. Calculate the current flowing through the detector.
Solution: I = V/R = 24V/600Ω = 0.04A = 40mA
Problem 2: Finding voltage drop
A security cable with resistance of 2Ω carries 0.5A to power a CCTV camera. Calculate the voltage drop along the cable.
Solution: V = I × R = 0.5A × 2Ω = 1V drop
Problem 3: Finding power consumption
An access control panel operates at 12V DC and draws 300mA. Calculate its power consumption.
Solution: P = V × I = 12V × 0.3A = 3.6W

## Slide 27
Circuit symbols: Resistors
Fixed resistor
Represented by a zigzag line or rectangle with leads. Common in voltage dividers and current-limiting applications.
Variable resistor
Shows a resistor with an arrow through it or a wiper contact. Used for adjustable settings in circuits.
Special resistors
Includes thermistors, photoresistors, and other environment-sensitive resistors used in sensing applications.
Recognising resistor symbols is fundamental for interpreting circuit diagrams in fire and security systems. These components control current flow, establish reference voltages, and form the backbone of most electronic circuits. In security applications, specialised resistors often serve as end-of-line devices for supervision of detection loops.
Understanding the specific function of each resistor type helps to identify critical components during system maintenance and troubleshooting.

## Slide 28
Digital Multimeter: The essential tool
Voltage measurement (V)
Connect in parallel with the component being measured. Select AC or DC mode appropriate for the circuit
Current measurement (A)
Connect in series with the circuit, breaking the path and inserting the meter. Requires proper range selection to avoid damage
Resistance measurement (Ω)
Only measure on de-energized circuits. Disconnect components from the circuit to get accurate readings
Continuity testing
Quickly verify electrical connections and identify breaks in wiring using the audible continuity function.

## Slide 29
Digital Multimeter: The essential tool
The digital multimeter is the most versatile diagnostic tool for electrical systems.
Proper measurement technique is critical both for accurate readings and safety, particularly when working with fire alarm and security systems that may have backup power sources.

## Slide 30
Using a Digital Multimeter: Safety first
Voltage rating
Ensure your multimeter is rated for the voltage being measured
Inspect equipment
Check probes and leads for damaged insulation or exposed metal.
Proper technique
Use one hand, when possible, to avoid creating a path for current through your body. Never measure current in parallel or resistance in energised circuits
De-energise when possible
When working on fire system circuits, follow proper isolation procedures before testing, especially when measuring resistance or testing components

## Slide 31
Measuring voltage with a Digital Multimeter
Setup
Set the multimeter to voltage mode (V) and select AC or DC as appropriate. Most fire and security systems use DC, but mains power supplies are AC.
For unknown voltages, start with the highest range and work down for better accuracy.
Connection
Connect the black probe to the common terminal (COM) and the red probe to the voltage terminal (V/Ω).
For DC measurements, red connects to the positive point and black to the negative or reference point.
Measurement
Touch probes to the circuit points across which you want to measure voltage. Hold firmly but avoid shorting adjacent components.
For fire alarm circuits, common measurements include checking 24V DC power rails and voltage across end-of-line resistors.

## Slide 32
Measuring current with a Digital Multimeter
Prepare the circuit
Switch off power and break the circuit at the point where you want to measure current flow.
Configure the multimeter
Set to current measurement mode (A or mA) and select an appropriate range.
Connect in series
Place multimeter in series with the circuit (current must flow through the meter).
Restore power and read
Power up the circuit and read the current value displayed.

## Slide 33
Measuring current with a Digital Multimeter
In fire and security systems, current measurements are essential for verifying standby and alarm currents drawn by devices.
This information is critical for proper power supply sizing and battery backup calculations required by BS 5839-1 for life safety systems and BS EN 50131-6 for intruder alarms.

## Slide 34
Measuring resistance and continuity
Resistance measurement
To measure resistance, first ensure the circuit is completely de-energised. Set the multimeter to resistance mode (Ω) and select an appropriate range if not auto-ranging.
Connect the probes across the component or circuit section, ensuring good contact. Read the displayed value, typically in ohms (Ω), kilohms (kΩ), or megohms (MΩ).
For accurate readings, components should ideally be disconnected from the circuit, as parallel paths can affect readings.
Continuity testing
Continuity testing is a specialised resistance test that verifies whether a path exists for current to flow. It's essential for checking cable integrity in security installations.
Set the multimeter to continuity mode (usually indicated by a sound wave symbol). Connect probes to the circuit ends being tested.
A continuous beep or very low resistance reading (typically <10Ω) indicates continuity. This function is particularly useful for tracing wire paths, finding breaks in cables, and verifying connections in fire alarm circuits.

## Slide 35
Measuring resistance and continuity

## Slide 36
Testing resistors with a multimeter
Preparation
Ideally, remove the resistor from the circuit or disconnect one end to prevent parallel paths from affecting the reading. Set the multimeter to resistance mode (Ω).
For resistors with values above 1kΩ, handling the leads can affect measurements due to body resistance, so hold only the insulated parts of the probes.
Measurement process
Touch the probes to the resistor leads. Polarity doesn't matter for standard resistors. Compare the reading with the expected value based on the colour code or marking.
Most resistors have a tolerance (typically ±5% or ±1%), so expect some variation from the nominal value. A reading far outside this range indicates a faulty component.
Security system application
In fire and security systems, end-of-line (EOL) resistors are critical for supervision of detection loops. These must be precisely valued (commonly 4.7kΩ or 10kΩ) to ensure proper alarm monitoring.
Always verify replacement EOL resistors with a multimeter before installation, as incorrect values can cause false alarms or failure to detect genuine alarm conditions.

## Slide 37
Testing capacitors with a multimeter
Safety first
Ensure capacitors are fully discharged before testing. Large capacitors in power supplies can hold dangerous charges even when disconnected. Discharge by connecting a resistor (1kΩ to 10kΩ) across the terminals
Using dedicated capacitance function
Modern multimeters often have a capacitance measurement function (usually marked with 'F' or 'nF'). Set to this range, connect probes to the capacitor terminals observing polarity for electrolytic types, and read the value
Analog testing method
Without a capacitance function, use resistance mode. The capacitor should initially show low resistance that gradually increases (charging). Reversed probes should show the same pattern (discharging then charging in opposite direction)
Identifying faulty capacitors
A capacitor showing permanent low resistance is shorted. One showing no resistance change (staying at infinite) is open circuit. Electrolytic capacitors with excessive leakage current are also defective

## Slide 38
Testing inductors with a multimeter
Resistance test
Set multimeter to resistance mode and measure across inductor terminals. A good inductor should show low resistance (typically a few ohms to tens of ohms). An open circuit reading indicates a broken winding.
Inductance measurement
Specialised multimeters include inductance measurement (marked with 'H' for henry). This function directly measures the inductor value, which is useful for identifying unmarked components.
Physical inspection
Visually inspect for burnt areas, mechanical damage, or overheating. In security systems, inductors may fail due to surges or overload conditions, leaving visible damage.
Practical application
In fire alarm systems, inductors are often found in power supply filter circuits and sounder circuits where they reduce electrical noise and improve circuit stability.

## Slide 39
Testing diodes and LEDs
Diode testing
Set the multimeter to diode test mode (usually marked with a diode symbol).
Connect the red probe to the anode and the black probe to the cathode to measure forward voltage drop.
A silicon diode typically shows 0.6-0.7V in forward bias. Reverse the probes (black to anode, red to cathode) to check reverse bias - should show "OL" (overload) indicating high resistance.
A shorted diode will show near-zero voltage in both directions. An open diode will show "OL" in both directions.

## Slide 40
Testing diodes and LEDs
LED testing
LEDs are tested similarly to diodes but have higher forward voltage drops:
Red LEDs typically 1.8-2.2V
Green 2.0-2.5V
Blue/white 2.5-3.3V.
Some multimeters can supply enough current in diode test mode to illuminate the LED, providing a visual confirmation of functionality. However, current-limiting resistors should be used for full brightness testing.
In fire alarm panels, status LEDs are critical indicators. Failed LEDs can lead to misinterpretation of system status, making regular testing essential.

## Slide 41
Capacitors: Energy storage elements
Energy storage
Stores electrical charge for later release
Signal filtering
Blocks DC while allowing AC to pass
Timing circuits
Controls time constants in oscillators
1
4
Power smoothing
Reduces ripple in power supplies

## Slide 42
Capacitors: Energy storage elements
Capacitors are fundamental components in virtually all electronic circuits, including fire and security systems.
They maintain stable voltage in power supplies, provide energy for alarm sounders during voltage dips, and help filter out electrical noise that could cause false alarms.
In security systems, capacitors often support backup power systems and help maintain circuit operation during brief power interruptions, providing critical continuity for life safety functions.

## Slide 43: Capacitors: Introduction
Definition
Devices that store electrical energy in an electric field between a pair of conductors separated by an insulating material (dielectric)
Construction
Two conductive plates separated by a dielectric material such as ceramic, paper, plastic, or electrolyte
Function
Store energy, block DC while allowing AC, filter signals, and timing operations
Applications
Power supply filtering, timing circuits, coupling/decoupling, and energy storage in security systems

## Slide 44: Capacitors: Uses
In fire and security systems, capacitors serve several critical functions:
stabilising power supplies by filtering out voltage fluctuations
creating time delays in alarm verification circuits
providing momentary backup power during brief interruptions.

## Slide 45: Capacitor construction and operation
Basic structure
A capacitor consists of two conductive plates (typically metal foil) separated by an insulating dielectric material. The plates store opposite charges when a voltage is applied, creating an electric field in the dielectric.
When connected to a voltage source, electrons accumulate on the negative plate and are depleted from the positive plate until the voltage across the capacitor equals the source voltage.
Charging and discharging
During charging, current flows until the capacitor reaches the source voltage. The charging rate follows an exponential curve, with the time constant determined by the circuit resistance and capacitance (τ = RC).
When discharged through a resistor, the voltage decreases exponentially. This predictable timing property is used in security system timing circuits, such as entry/exit delays in intruder alarms.

## Slide 46: Factors affecting capacitance
Plate area
Capacitance increases with larger plate area
Plate separation
Capacitance increases as plate separation decreases
Dielectric material
Capacitance increases with higher dielectric constant

## Slide 47: Units of capacitance
In fire alarm systems, you'll typically encounter microfarad (µF) capacitors in power supply filtering circuits and nanofarad (nF) to microfarad range in timing circuits for alarm verification. Capacitors are most commonly seen in end-of-line devices used to monitor circuit integrity.
They may also appear within PCBs for noise suppression or timing functions, but these are not typically serviced or tested by technicians.
Security system digital components often use smaller value capacitors (pF to nF range) for decoupling to prevent electrical noise interference.

## Slide 48: Types of capacitors and their applications
Electrolytic capacitors
Polarised capacitors with high capacitance values (1µF to thousands of µF). Used in power supply filtering in security panels. Relatively high tolerance (±20%) and limited lifespan. Essential for smoothing rectified AC into stable DC for sensitive security electronics.
Ceramic capacitors
Non-polarised with small to medium capacitance (pF to µF). Used for decoupling and bypassing in control circuits. Temperature stable types are critical in fire detection systems where environmental conditions vary. Compact size makes them ideal for crowded PCBs.
Film capacitors
Excellent stability and reliability with low losses. Commonly used in timing circuits for entry/exit delays and oscillators in security systems. Their precision and temperature stability make them ideal for circuits where consistent timing is critical to system operation.

## Slide 49: Capacitor polarity and safety
Identifying polarity
Electrolytic and tantalum capacitors are polarised – they must be connected with the correct polarity. Look for negative (−) stripe, indentation, or shorter lead to identify the negative terminal.
Voltage ratings
Capacitors have maximum voltage ratings that must not be exceeded. In security systems, always use capacitors rated at least 25% higher than the maximum circuit voltage.
Risk of explosion
Electrolytic capacitors can explode if reverse-connected or over-voltaged. Modern types include safety vents but can still cause circuit damage or injury.
Stored energy
Capacitors store energy even when disconnected. Always discharge capacitors before handling, particularly in power supply circuits of alarm panels.

## Slide 50: Capacitor applications in security systems
Power supply filtering
Large electrolytic capacitors smooth rectified AC into stable DC, reducing ripple voltage that could cause interference in sensitive alarm circuits. Typical values range from 470µF to 4700µF depending on current requirements.
Smaller ceramic capacitors (0.1µF to 0.01µF) provide local decoupling to prevent digital noise from affecting analog circuits.
Timing circuits
Capacitors combined with resistors create predictable time delays for entry/exit timers, alarm verification, and door release timing. Film capacitors offer the stability needed for precise timing.
In fire systems, timing circuits may control sequential evacuation or delay verification to prevent false alarms from transient smoke or dust.
Coupling and Blocking
Capacitors block DC while passing AC signals, useful in audio circuits for alarm sounders and voice evacuation systems. They can also couple signals between stages while blocking DC bias voltages.
In addressable fire systems, capacitors help shape the digital communication signals that transmit data between the control panel and detectors.

## Slide 51: Capacitor calculations: Determining values
Reading capacitor markings
Modern capacitors typically show value and voltage directly. Older or smaller types use codes: three-digit code indicates value in pF (first two digits followed by number of zeros), while letter codes indicate tolerance (J=±5%, K=±10%, M=±20%).
Example: "104K" means 10 followed by 4 zeros = 100,000pF = 0.1µF with ±10% tolerance.
Conversion between units
1F = 1,000,000µF = 1,000,000,000nF = 1,000,000,000,000pF
To convert: move decimal point 6 places for µF to F, 3 places for nF to µF, and 3 places for pF to nF.
Calculating time constants
The time constant τ = R × C (where R is in ohms and C is in farads) gives the time in seconds for a capacitor to charge to 63% or discharge to 37% of its final value.
In fire system verification delays, this formula helps determine the appropriate component values to achieve required timing.

## Slide 52
Capacitor safety considerations
500V
Voltage rating
Maximum voltage a capacitor can withstand before dielectric breakdown occurs
60s
Discharge time
Time capacitors can hold charge after power is removed
5-10
Safety factor
Recommended voltage derating for reliable operation
Capacitors can store a charge long after a circuit is powered down, presenting shock hazards. This is particularly true for high-value electrolytic capacitors in power supplies and backup systems. Always discharge capacitors through an appropriate resistor (1kΩ-10kΩ) before working on circuits.
In fire and security systems, capacitors in alarm sounders and strobe circuits can store enough energy to cause injury. Some larger filter capacitors in power supply sections of control panels may hold lethal charges. Never assume a disconnected circuit is safe without verifying discharge.

## Slide 53
Inductance: Introduction
Definition
Property of a conductor to oppose changes in current by inducing a voltage
Basic principle
Current flowing creates a magnetic field; changes in this field induce voltage
Construction
Typically, a coil of wire, often around a magnetic core material
Function
Stores energy in magnetic field, blocks AC while passing DC, filters signals

## Slide 54
Inductance: Uses
In fire and security systems, inductors play several important roles.
They help:
filter noise from power supplies
prevent false triggering from electromagnetic interference
are key components in communication circuits that connect detectors and control panels.

## Slide 55
Inductor applications in security systems
Power supply filtering
Inductors combined with capacitors form LC filters that remove noise and ripple from DC power supplies, ensuring clean power for sensitive detection circuits
EMI suppression
Common-mode chokes and ferrite beads prevent electromagnetic interference from entering or leaving security system components, reducing false alarms from external noise sources
RF Circuits
Inductors tune wireless communication circuits in wireless sensors and alarm transmitters, optimising reception and transmission of security signals
Magnetic sensors
Specialised inductors form the core of proximity and position sensors used in door and window security contacts, detecting changes in magnetic fields when protected areas are breached

## Slide 56
Inductor applications in security systems
Inductors play crucial roles in maintaining signal integrity and power quality in security systems, helping prevent both false alarms and missed detections that could compromise safety.

## Slide 57
Inductor construction and operation
Core materials
Air: No magnetic amplification, lower inductance
Iron: High permeability, increases inductance
Ferrite: Good at high frequencies, low losses
Powdered Iron: Stable, high current handling
Winding configuration
Single layer: Better for high frequencies
Multilayer: Higher inductance in smaller space
Toroidal: Efficient field containment
Bifilar: Reduces parasitic effects
Operational principles
When current flows through a coil, a magnetic field forms around it. The magnetic field strength is proportional to both current and the number of turns. When current changes, the changing magnetic field induces a voltage opposing the change.

## Slide 58
Inductor construction and operation
In fire alarm systems, inductors in filter circuits help protect sensitive detection components from electrical noise and transients that could cause false alarms.
Their ability to resist rapid current changes also helps stabilise power supplies during line voltage fluctuations.

## Slide 59
Factors affecting inductance
Number of turns
Inductance increases with the square of the number of turns
Core material
Ferromagnetic cores dramatically increase inductance
Core dimensions
Larger core cross-section and shorter magnetic path
increase inductance

## Slide 60
Factors affecting inductance
The inductance (L) of a coil is proportional to µN²A/l, where:
µ is the magnetic permeability of the core
N is the number of turns
A is the cross-sectional area of the core
l is the length of the coil.
This relationship explains why small adjustments to coil parameters can significantly affect inductance.
In security system applications, inductor design must balance size constraints with performance requirements.
Power supply filter inductors need high current capacity without saturation, while signal inductors must minimise electromagnetic interference without introducing excessive resistance.

## Slide 61
Back EMF in inductors
Current flow
Steady current creates
stable magnetic field
Circuit interruption
Current path suddenly broken
Field collapse
Magnetic field collapses rapidly
Voltage spike
High back EMF generated:
V = L × (dI/dt)
4

## Slide 62
Back EMF in inductors
Back EMF is a critical consideration in security systems that contain relay coils or solenoids, such as magnetic door locks and fire suppression system actuators.
When de-energised, these inductive components generate voltage spikes that can damage sensitive electronic components if not properly suppressed.
The magnitude of back EMF is proportional to the inductance and the rate of current change.
In practical terms, larger coils and faster switching create larger voltage spikes that require more robust protection measures.

## Slide 63
Suppressing back EMF
Flyback diodes
The most common suppression method places a diode in reverse bias across the inductor. When current stops, the back EMF forward biases the diode, providing a path for the coil's energy to dissipate safely. This limits the voltage spike to approximately the diode's forward voltage drop.
RC Snubbers
A resistor and capacitor in series across the inductor creates a damped discharge path. This approach is better for AC circuits where diodes cannot be used. The resistor limits the discharge current while the capacitor absorbs the energy from the collapsing field.
Varistors/TVS
Voltage-dependent resistors that become conductive above a threshold voltage. They provide bidirectional protection and faster response than diodes, making them suitable for protecting sensitive circuits from inductive spikes in critical safety systems.

## Slide 64
Suppressing back EMF
Proper back EMF suppression is essential in fire and security systems to prevent:
false triggering of sensors
protect microcontrollers that control the system logic.

## Slide 65
Self-induced vs Mutual-induced EMF
In security systems, both types of induced EMF must be considered.
Self-induced EMF affects the performance of solenoids in electric locks and relay-controlled devices.
Mutually induced EMF can cause crosstalk between adjacent signal wires, potentially creating false triggers in sensor circuits.
Proper shielding, twisted pair wiring, and physical separation are techniques used to minimise unwanted mutual induction effects in critical security and fire alarm systems.

## Slide 66
Transformers: Introduction
Definition
Electrical device that transfers energy between circuits through electromagnetic induction
Construction
Two or more coils (windings) sharing a common magnetic core
Function
Transfers AC power between circuits while changing voltage and current levels
3
Isolation
Provides electrical isolation between input and output circuits

## Slide 67
Transformers: Uses
Transformers are essential components in fire and security systems, providing:
power conversion
isolation
signal coupling functions.
They allow security equipment to operate from standard mains power while maintaining electrical safety through isolation.
In power supply sections, transformers convert low-voltage AC to lower voltages suitable for electronic circuits, providing inherent protection against power line surges and helping to maintain electrical safety standards required in life safety systems.
They are critical components in security and fire alarm systems, providing electrical isolation between detection circuits and control equipment while allowing signals to pass. This isolation protects sensitive microcontrollers from electrical noise and potential damage from field wiring faults.

## Slide 68
Transformers: Energy transfer devices
Electromagnetic coupling
Energy transfer without direct electrical connection
Voltage transformation
Step up or step down voltage levels
3
Electrical isolation
Separate circuits while transferring power
Impedance matching
Optimise power transfer between circuits

## Slide 69
Transformer construction and basic operation
Basic components
Operating principle
The transformer operates on the principle of electromagnetic induction:
Core materials
Primary winding: Receives input power
Secondary winding: Delivers output power
Core: Provides magnetic path between windings
Insulation: Prevents electrical contact
AC current in primary creates changing magnetic field
Magnetic field couples to secondary through core
Changing field induces voltage in secondary
Voltage ratio proportional to turns ratio
Laminated silicon steel: Power transformers
Ferrite: High-frequency applications
Air core: Very high frequencies
Toroidal: Efficient field containment

## Slide 70
Transformer construction and basic operation
In security systems, transformers provide critical isolation between line-voltage circuits and low-voltage control equipment.
This protects both users and sensitive electronics while enabling reliable power distribution throughout the system.

## Slide 71
Transformer applications in security systems
Power supplies
Step-down transformers convert 120/240V AC mains to lower voltages (12V, 24V) required by security equipment while providing galvanic isolation from potentially dangerous utility power.
Signal isolation
Pulse transformers isolate digital communication lines between sensors and control panels, protecting against ground loops and electrical noise that could cause false alarms.
Data communications
Transformers in network interfaces isolate Ethernet connections to security cameras and access control systems, preventing damage from ground potential differences.
Audio circuits
Audio transformers in intercom and public address systems provide impedance matching and isolation for clear communication during emergency situations.

## Slide 72
Transformer applications in security systems
Transformers play a crucial role in maintaining electrical safety and signal integrity in security systems, particularly in installations that span multiple buildings or cover large areas, where ground potential differences can be substantial.

## Slide 73
Transformer current relationship
1:1
Equal Turns
Same current in both windings (ideal transformer)
1:2
Step-Up Ratio
Secondary current half of primary
2:1
Step-Down Ratio
Secondary current twice primary
In an ideal transformer, the relationship between primary and secondary currents is inversely proportional to the turns ratio: Is/Ip = Np/Ns. This reflects the conservation of power across the transformer (P = VI), where power input equals power output in an ideal transformer.
This principle is critical when designing power supplies for security systems. As voltage is stepped down, available current increases proportionally. For example, a security system drawing 2A at 12V might be powered by a transformer converting 120V AC at 0.2A to 12V AC at 2A, maintaining the same power level while providing a safe, usable voltage.
Understanding this relationship helps engineers specify transformers with adequate current capacity for the connected load.

## Slide 74
Power in transformers
Input Power
Pin = Vp × Ip × cos(φ)
Power Losses
Core losses + Copper losses + Stray losses
Output Power
Pout = Vs × Is × cos(φ)
3
Efficiency
η = Pout / Pin × 100%

## Slide 75
Power in transformers
In real transformers, power losses occur through various mechanisms: core losses from hysteresis and eddy currents in the iron core, there are:
copper losses from resistance in the windings
stray losses from leakage flux and capacitive effects.
These losses manifest as heat, which must be managed to prevent overheating.
In security system applications, transformer efficiency affects both operating costs and heat generation.
Higher efficiency transformers run cooler and waste less energy, an important consideration for systems that operate continuously, such as those used in fire detection and building security.

## Slide 76
Semiconductor basics
1
Semiconductors vs. Conductors/Insulators
Semiconductors occupy the middle ground between conductors and insulators. They typically have four valence electrons, forming covalent bonds with neighboring atoms. This crystal structure conducts poorly at low temperatures, but conductivity increases with temperature as electrons gain energy and break free from their bonds.
2
Silicon: The foundation material
Silicon (Si) is the most widely used semiconductor material due to its abundance, stable properties, and ability to form a high-quality oxide layer. Its four valence electrons create a tetrahedral crystal structure that can be precisely modified through doping processes to create useful electronic devices.
3
Doping: Creating useful semiconductor types
Pure semiconductors can be modified by adding impurity atoms (doping): N-type semiconductors contain donor atoms (like phosphorus) that provide extra electrons. P-type semiconductors contain acceptor atoms (like boron) that create "holes" - absence of electrons that behave like positive charges.

## Slide 77
Semiconductor basics
Understanding semiconductor properties is fundamental to working with electronic components in security systems.
They can be from simple diodes that protect circuits to complex integrated circuits that process sensor signals and control system responses.

## Slide 78
Diode applications in security systems
Rectification
Diodes convert AC to DC in power supplies for control panels and sensors. In bridge rectifier configurations, four diodes convert both halves of the AC cycle to DC, providing efficient power conversion for system operation.
Protection circuits
Reverse polarity protection diodes prevent damage from incorrect battery connections. Transient voltage suppressors (specialised diodes) protect against lightning-induced surges on sensor wiring and power lines.
Signal processing
Diodes in peak detection circuits capture maximum values from sensor outputs. Clamping diodes limit signal voltages to safe levels for analogue-to-digital converters in control panels.
Isolation and Steering
Diodes isolate multiple inputs to prevent backfeeding between circuits. In addressable fire alarm systems, diodes direct current flow to ensure proper device polling and response.

## Slide 79
Diode applications in security systems
Diodes are among the most versatile components in security systems, providing essential functions in power, protection, and signal processing circuits throughout the system architecture.

## Slide 80
Light Emitting Diodes (LEDs)
Light Emitting Diodes operate on the principle of electroluminescence. When forward biased, electrons cross the junction and recombine with holes, releasing energy in the form of photons (light). The specific semiconductor materials used determine the photon energy and thus the color of light emitted.
Unlike regular diodes, LEDs typically have higher forward voltage drops: red ~1.8V, green ~2.1V, blue ~3.3V. In security systems, LEDs provide critical status indication for power, armed status, zones, and fault conditions, with different colours conveying different information.

## Slide 81
LED characteristics and applications
Key characteristics
Security system applications
Forward voltage varies by color (1.8-3.6V)
Requires current limiting (typically 5-20mA)
Directional light output (beam angle varies)
Long life (50,000+ hours)
Low heat generation
Available in various packages (through-hole, SMD)
Status indication (Power, Armed, Ready)
Zone status and fault indication
Communication activity indicators
Emergency lighting
Visual alarm indicators
IR LEDs for motion detectors
Keypad illumination

## Slide 82
LED characteristics and applications
LEDs in security systems provide critical visual feedback to both users and technicians. Their color coding follows industry standards: green typically indicates normal operation, red indicates alarm conditions or armed status, yellow/amber indicates trouble or fault conditions, and blue is often used for special functions or communication activity.
Current limiting is essential for LED operation. A series resistor calculated as: R = (Vsupply - VLED)
ILED prevents excessive current that would damage the device.

## Slide 83
LED identification and polarity
Through-hole LED polarity
Standard LEDs have several identifiers: The cathode lead (negative) is typically shorter than the anode lead. The LED package has a flat spot on the cathode side. The internal metal structure is larger on the cathode side (visible through transparent packages).
SMD LED polarity
Surface-mount LEDs usually have a cathode marked by a dot, notch, or band. The PCB silkscreen often includes a marker showing orientation. Some packages have a green cathode end and a notched corner for orientation.
LED displays and arrays
Multi-segment displays and LED arrays typically indicate common anode or common cathode configuration in documentation. Pin 1 is often identified by a dot or notch on the package, with datasheets providing complete pinout information.

## Slide 84
LED identification and polarity
Correct polarity identification is essential when servicing LED indicators in security systems, as reversed connections will prevent operation but typically won't damage the LED itself.

## Slide 85
NPN Bipolar junction transistors
Structure
N-type collector, P-type base, N-type emitter
Current control
Small base current controls larger collector current
Amplification
Current gain (β) = IC/IB (typically, 50-200)
Switching
Operates in cutoff, active, or saturation regions

## Slide 86
NPN Bipolar junction transistors
NPN transistors are fundamental amplifying and switching components in security system circuits.
A small current flowing from base to emitter controls a much larger current flowing from collector to emitter, providing both amplification and switching capabilities.
In security applications, transistors amplify weak sensor signals to detectable levels and switch higher-current loads like relays, solenoids, and alarm sounders based on low-current control signals from microcontrollers. They are also key components in voltage regulators that provide stable power to sensitive detection circuits.

## Slide 87
Transistor operating regions
1
Cutoff region
No base current → No collector current
Active region
Linear relationship between IB and IC
Saturation region
Maximum collector current for given circuit

## Slide 88
Transistor operating regions
Understanding transistor operating regions is crucial for designing circuits in security systems.
In the cutoff region, the transistor acts as an open switch, used when a device needs to be completely off.
The active region enables linear amplification of sensor signals.
The saturation region is used for switching applications, where the transistor acts as a closed switch with minimal voltage drop.
In alarm panels, transistors often operate in either cutoff or saturation to control indicator LEDs, relays, and buzzers.
In sensor interfaces, they may operate in the active region to amplify small signals from detection elements before digital processing.

## Slide 89
NPN Transistor applications
Switching applications
Transistors control higher-current devices like alarm bells, strobes, and magnetic door locks based on low-current signals from microcontrollers, providing electrical isolation and current amplification.
Signal amplification
Weak signals from sensors like smoke detectors, passive infrared motion detectors, and glass break detectors are amplified to levels that can be accurately processed by analog-to-digital converters.
Logic circuits
Transistors implement basic logic functions in interface circuits between different sections of security systems, providing level shifting and signal conditioning between components operating at different voltages.
Voltage regulation
Multiple transistors in voltage regulator circuits provide stable power to sensitive components, ensuring consistent performance regardless of input voltage fluctuations or load changes.

## Slide 90
NPN Transistor applications
Transistors are versatile components that perform essential functions throughout security and fire alarm systems, from sensor interfaces to output control circuits.

## Slide 91
Transistor identification and polarity
Common package types
The package type indicates power handling capability and provides clues to terminal identification. Always verify with manufacturer datasheets, as incorrect connections can damage both the transistor and surrounding components.
Terminal identification
Terminal arrangements vary by package type:
.
TO-92: Small plastic package for low-power applications
TO-220: Larger package with metal tab for heat dissipation
SOT-23: Small surface-mount package for modern circuits
TO-3: Metal can package for high-power applications
TO-92: Looking at flat side, typically E-B-C from left to right
TO-220: Usually E-B-C when viewed from front
SOT-23: Requires datasheet verification; no standard arrangement

## Slide 92
Transistor identification and polarity
When servicing security systems, correctly identifying transistor types and terminals is essential.
Many security components use custom-designed circuit boards where transistors perform specific functions.
Replacement requires exact matching of specifications and proper orientation to maintain system reliability.

## Slide 93
Basic transistor testing
Base-emitter junction test
Using the multimeter's diode test function, connect the positive (red) probe to the base and negative (black) probe to the emitter. A silicon NPN transistor should show a reading of 0.6-0.7V, indicating a forward-biased junction. Reversing the probes should show no conduction (OL reading).
Base-collector junction test
Connect the positive probe to the base and negative probe to the collector. Similar to the B-E test, a reading of 0.6-0.7V indicates a healthy junction. Reversing the probes should show no conduction. For PNP transistors, the probe polarities would be reversed from those used for NPN testing.
Collector-emitter conduction test
With no connection to the base, there should be no conduction between collector and emitter (high resistance or OL reading). When the base-emitter junction is forward biased with a finger touch or resistor to positive voltage, the C-E path should conduct, showing a low resistance reading.
These basic tests can quickly identify the most common transistor failures in security system circuits without requiring specialised equipment.

## Slide 94
Integrated circuits in security systems
Microcontrollers
The "brains" of modern security systems, these programmable devices process sensor inputs, control outputs, and manage communication. They run firmware that implements the system's features, including zone monitoring, user interface, and alarm logic.
Operational amplifiers
Versatile analog ICs that condition signals from various sensors. In security applications, they amplify small signals, create voltage comparators for threshold detection, and buffer signals between different system sections.
Voltage regulators
Provide stable power to sensitive components regardless of input voltage fluctuations or load changes. Linear and switching regulators generate the various voltage rails needed by digital and analog circuits throughout the system.
Specialised security ICs
Purpose-built integrated circuits that implement specific security functions like motion detection signal processing, glass break analysis, smoke detector sensitivity control, and encryption for wireless communications.
While discrete components like resistors, capacitors and transistors form the foundation of electronic circuits, integrated circuits provide the complex functionality required by modern security and fire protection systems.

## Slide 95
Digital logic in security systems
Input processing
Logic gates combine multiple sensor inputs using AND, OR, and NOT functions to determine alarm conditions. For example, AND gates ensure multiple criteria are met before triggering, reducing false alarms.
State maintenance
Flip-flops and latches maintain system states like armed/disarmed or zone status. These bistable circuits hold their state until deliberately changed, providing system memory even during brief power interruptions.
Timing functions
Counters and timers control sequential operations like entry/exit delays, alarm cutoff timing, and communication protocols. Crystal-controlled oscillators provide precise timing references for these functions.
Output control
Decoder and driver ICs convert digital signals to the specific formats needed to control displays, relays, sounders, and communication interfaces.

## Slide 96
Digital logic in security systems
Digital logic provides the decision-making capability in security systems, determining when conditions require an alarm and controlling the system's response based on programmed parameters and user inputs.

## Slide 97
Fire alarm system component overview
Control panel
The central processing unit of the system
Detection devices
Smoke, heat, flame, and gas detectors
3
Alarm devices
Sounders, strobes, and voice evacuation
4
Circuit infrastructure
Wiring, modules, and power supplies
Fire alarm systems integrate electronic and electrical components into a life safety network.

## Slide 98: Summary
You should now be able to:
Understand basic electrical and electronic science principles relevant to protection systems
Be able to apply Ohm’s Law in protection systems
Understand the behaviour of basic electrical and electronic components used in protection systems

## Slide 99
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.