## Slide 1
Occupational Specialism: Protection Systems Engineering
K1.18 Maintenance of older systems and installations
PowerPoint 18: Maintenance of older systems and installations

## Slide 2: Introduction
This session focuses on the critical task of identifying legacy systems that may not comply with current regulations, and how to effectively assess and report on their condition and suitability for continued operation.
We'll explore methodologies for:
evaluation
common compliance issues
risk assessment frameworks, and
strategies
to maintain or upgrade these systems to meet modern standards whilst balancing operational requirements and budgetary constraints.

## Slide 3: Objectives
By the end of this session, you should be able to:
Understand how older systems and installations may differ from current British Standards and codes of practice.
Understand common signs of non-compliance, obsolescence, and reduced suitability for continued service.
Complete inspections that identify non-compliance, assess condition, and report on suitability for ongoing use, including recommendations for upgrade or replacement.

## Slide 4
Overview
Ageing infrastructure
Many industrial facilities operate equipment installed decades ago, designed to standards that have since evolved significantly.
Regulatory evolution
Health, safety and environmental regulations undergo continuous updates, creating compliance gaps for systems designed to previous standards.
Maintenance complexity
Obsolete parts, limited documentation and loss of institutional knowledge makes maintaining older systems increasingly challenging.
Economic pressures
Balancing the cost of replacement against continued maintenance presents difficult decisions for engineering teams.

## Slide 5
Regulatory framework overview
Primary legislation
Health and Safety at Work Act, etc.
UK Regulations
PUWER, LOLER, EAW Regulations
Approved Codes of Practice
HSE guidance and industry standards
Industry Standards
BS, EN, ISO specifications and guidance
Corporate standards
Internal policies and procedures

## Slide 6
Regulatory framework overview
Understanding this hierarchy is crucial when evaluating older systems, as compliance requirements may exist at multiple levels.
When conducting assessments, use the most current version of all applicable regulations to identify where legacy systems may fall short of contemporary requirements.

## Slide 7
Identification methodology
Visual inspection
  Check condition of equipment, cabling, containment, labels, and fixings.
  Look for signs of damage, corrosion, water ingress, or poor workmanship.
Functional testing
  Confirm devices still operate correctly (detectors activate, sounders work, locks release, cameras record).
  Note any components that show degraded or inconsistent performance.
Comparison against current standards
  Identify where the system does not meet current BS 5839, BS EN 50131, BS EN 50132/33 requirements.
  Note: British Standards are not applied retrospectively — non-compliance doesn’t always mean “immediate replacement”.

## Slide 8
Identification methodology
Assessment of suitability
  Judge whether the system remains safe, effective, and reliable for its intended purpose.
  Highlight obsolescence, unavailable spare parts, or unsupported software.
Reporting
  Record condition and suitability in reports or logbooks.
  Make recommendations for remedial action, phased upgrades, or replacement only where justified.

## Slide 9
Common non-compliance areas
Cabling and Containment
Incorrect cable type (non–fire-resistant or non–LSZH where required).
Poor or loose terminations.
Inadequate cable support (no fire clips, plastic trunking only).
Lack of segregation from mains or other services.
Modifications and Additions
New devices added without re-commissioning.
Non-approved components used.
Programming changes not recorded or tested.
Devices and Labelling
Detectors or call points incorrectly sited.
Sounders/VADs not achieving coverage.
Devices not labelled or incorrectly identified on zone charts.
Inaccessible or hidden devices (above ceilings, blocked by fixtures).
Documentation and Certification
Missing as-fitted drawings or zone charts.
No commissioning certificate.
Logbook not maintained.
Variations not documented or signed off.

## Slide 10
Assessment parameters
Physical condition
Evaluate visible signs of deterioration, including corrosion, damage, wear patterns, and ad-hoc modifications.
Performance data
Analyse operational metrics including efficiency, reliability, failure frequency, and maintenance requirements.
Documentation status
Assess completeness and accuracy of technical documentation, operating procedures, and maintenance records.
Operational feedback
Gather input from operators and maintenance personnel regarding usability, reliability, and known issues.
Safety features
Evaluate guarding, emergency stops, warning systems, and other protective measures against current standards.

## Slide 11
Technical assessment methods
Visual inspection
Structured checklist-based approach
Documentation
Conformance to installation standards
Functional testing
Performance against specifications
Safety function verification
Electrical testing
Battery calculations
Load testing
Voltage and current testing
Physical checks
Heights and locations of devices
Alerts activating on CIE
Signalling devices
Input/outputs

## Slide 12
Comprehensive reporting structure
System details
Site name, system type (fire, intruder, CCTV, access, etc.), date of service, engineer name.
Test results
Devices tested (detectors, call points, sounders, locks, cameras).
Measured values (sound levels, PSU load, battery capacity, CCTV recording checks).
Pass/fail notes (but always with actual measured data).
Actions and recommendations
Immediate remedials (done on site).
Required follow-up works.
Upgrade/replacement suggestions where appropriate.
Sign-off and records
Engineer signature, client acknowledgment.
Logbook entry and certificate issued (where required).
Non-compliances / defects
Clear list of issues (e.g. poor cabling, failed detectors, blocked sounders).
Reference to applicable standard (e.g. BS 5839-1, BS EN 50131).

## Slide 13
Remediation options analysis
1. Repair / Upgrade
Fix or replace faulty devices (e.g. detector, sounder, PSU, lock, camera).
Targeted upgrade where parts are obsolete, but the rest of the system is sound.
2. Replace
Full system replacement where equipment is beyond economic repair or cannot meet current standards.
Examples: obsolete fire panels, unsupported intruder panels, analogue CCTV needing digital conversion.
3. Mitigate / Manage risk
Temporary measures until permanent works can be carried out.
Examples: increase frequency of testing, use fire watch patrols, restrict access to affected areas, or enhance manual security checks.

## Slide 14
Decision-making framework
1
Regulatory compliance status
Evaluate severity of non-compliance issues
2
Risk assessment outcomes
Consider safety, environmental and operational risks
Economic analysis
Compare lifecycle costs of available options
Operational impact
Assess downtime and production consequences

## Slide 15
Decision-making framework
This decision-making framework ensures that all relevant factors are systematically considered when determining the optimal approach for each legacy system.
The process should involve key stakeholders including engineering, operations, safety, and financial teams to ensure all perspectives are adequately represented.
Documentation of the decision-making process is essential, particularly for cases where full compliance cannot be immediately achieved, to demonstrate due diligence and reasoned judgment.

## Slide 16
Documentation and record-keeping
Proper documentation is essential for demonstrating due diligence in the management of legacy systems. Records should include:
assessment reports
risk analyses
decision justifications
implementation plans, and
verification of completed actions.
This documentation serves both as protection in regulatory discussions and as valuable reference material for future engineering decisions.
Best practice includes establishing a central repository for all assessment documentation with appropriate indexing and version control. Regular audits of the documentation system should be conducted to ensure completeness and accuracy of records.

## Slide 17
Temporary operation protocols
Extra checks
Increase the frequency of manual tests (e.g. daily fire alarm call point check, extra intruder set/unset confirmation)
Clear user instructions
Brief staff on what to do if a system fault occurs (e.g. how to raise a fire alarm manually, alternative entry/exit control)
Closer supervision
Assign responsibility for monitoring systems more actively until repairs are complete (e.g. fire watch patrols, security staff watching CCTV more closely)
Workarounds
Use temporary equipment or
re-route functions where possible (e.g. standalone sounder, temporary CCTV recorder, door held open under supervision)

## Slide 18
Temporary operation protocols
When non-compliant systems must remain in operation temporarily, structured protocols provide essential risk mitigation.
These protocols should be formally documented, with clear ownership and accountability for implementation.
Time limits for temporary operation should be established, with extension procedures requiring senior management approval.

## Slide 19: Summary
You should now be able to:
Understand how older systems and installations may differ from current British Standards and codes of practice.
Understand common signs of non-compliance, obsolescence, and reduced suitability for continued service.
Complete inspections that identify non-compliance, assess condition, and report on suitability for ongoing use, including recommendations for upgrade or replacement.

## Slide 20
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.