## Slide 1
Occupational Specialism: Electrotechnical Engineering
K1.17 Types of electrotechnical system maintenance
PowerPoint 1.17: Planned preventative maintenance (PPM) and reactive maintenance
Notes: https://electrical.theiet.org/wiring-matters/years/2023/94-march-2023/isolation-and-switching-for-mechanical-maintenance/
https://electrical.theiet.org/wiring-matters/years/2022/91-july-2022/electrical-maintenance-a-framework-for-good-practice/
https://www.theiet.org/media/9451/safe-maintenance-of-equipment-including-machinery.pdf

## Slide 2: Introduction
What could happen if an electrical system in a building had no maintenance carried out over successive years?
Notes: Lights stop working unexpectedly
Fire alarms fail to sound
Equipment overheats or breaks
Safety risks increase
Costly emergency repairs needed

## Slide 3: Objectives
By the end of this session, you should be able to:
Identify the two main types of maintenance: planned preventive and reactive
Explain legal responsibilities and industry standards relating to electrical system maintenance
Compare the advantages and limitations of PPM and reactive approaches

## Slide 4: Introduction to system maintenance
Maintenance in electrotechnical systems is essential to ensure continued safety, reliability, and compliance with legal standards. Over time:
components can wear
connections can loosen, and
protective devices may degrade.
Without routine checks and timely intervention, faults may go unnoticed, increasing the risk of failure, downtime, or even electric shock or fire.
Notes: Emphasise the importance of maintenance in both domestic and industrial settings.
Give a few relatable examples: e.g. checking RCDs in homes, or regular servicing of emergency lighting in a public building.
Highlight that maintenance is not just about fixing things when they break, but about preventing failure.
There are two main approaches to maintenance: planned preventative maintenance (PPM) and reactive maintenance, each with its own advantages and limitations. Choosing the right approach depends on the type of system, environment, and legal responsibilities.
Introduce the two maintenance strategies briefly (PPM and reactive), which will be explored in later slides.

## Slide 5: Two approaches to maintenance
There are two main approaches to maintenance:
planned preventative maintenance (PPM)
reactive maintenance.
Each has its own advantages and limitations.
Choosing the right approach depends on the type of system, environment, and legal responsibilities.
Notes: Emphasise the importance of maintenance in both domestic and industrial settings.
Give a few relatable examples: e.g. checking RCDs in homes, or regular servicing of emergency lighting in a public building.
Highlight that maintenance is not just about fixing things when they break, but about preventing failure.
Introduce the two maintenance strategies briefly (PPM and reactive), which will be explored in later slides.

## Slide 6: Planned preventative maintenance (PPM)
Planned preventative maintenance (PPM) involves scheduled inspections, tests and servicing to keep systems in safe working condition.
The aim is to identify and fix issues before they lead to failure.
Activities may include tightening connections, changing lamps, servicing motors.
PPM is often based on manufacturer instructions, industry standards like BS7671, and site-specific risk assessments.
It helps extend equipment life. By taking a proactive approach, PPM can reduce unexpected downtime and ensure compliance with legal obligations.
Notes: Explain that PPM is a proactive approach.
Mention common examples: periodic inspection of distribution boards, testing emergency lighting, and thermal imaging in commercial settings.
Link back to earlier learning: many of the tasks carried out in initial verification become part of ongoing maintenance.
If available, show an example maintenance schedule or O&M manual excerpt to reinforce structure and frequency.

## Slide 7: Benefits of planned preventative maintenance
PPM offers several important benefits to both the user and the electrical system.
Improved safety: Regular checks reduce the risk of electrical faults or fires.
Increased reliability: Equipment is less likely to fail without warning.
Cost savings: Preventing problems is often cheaper than emergency repairs or replacing damaged equipment.
Compliance: Helps meet legal duties under the Electricity at Work Regulations.
Longer equipment lifespan: Components stay in good condition for longer.
Improved planning: Maintenance can be scheduled to minimise disruption.
Notes: Ask learners: “Can you think of examples where maintenance would have prevented a fault?”
Discuss cost savings in real terms: reduced call-outs, fewer replacements.
Reinforce link to legal responsibilities—maintenance is not optional under health and safety law.
If possible, share a short case study or incident report where a lack of PPM led to failure or injury.

## Slide 8: Reactive maintenance
Reactive maintenance is the process of repairing or replacing components only after they have failed.
This approach is commonly used in low-risk systems or when downtime has minimal consequences.
While it may seem cost-effective initially, repeated failures can result in more disruption and higher costs over time.
Notes: Highlight that reactive maintenance is not inherently wrong but is more suitable for systems where reliability is less critical. Give real-world examples such as replacing failed lamps in non-essential areas. Ask learners to consider when reactive maintenance might be appropriate or risky.

## Slide 9: Responsibilities in maintenance regimes
Maintenance must be managed to ensure safety, reliability, and legal compliance.
Employers ensuring systems are maintained safely (Electricity at Work Regulations 1989).
Duty holders scheduling and recording maintenance activities.
Competent persons carrying out the work in line with standards.
Notes: Stress the legal obligations under EAWR 1989 and the need for qualified persons. Reinforce the link between maintenance and duty of care. Encourage learners to identify who would take on these roles in different workplace settings.
https://electrical.theiet.org/wiring-matters/years/2021/86-july-2021/setting-up-a-basic-electrical-maintenance-regime/

## Slide 10: Documentation and record-keeping
Proper maintenance includes documenting all actions taken.
Maintenance logs.
Inspection reports.
Fault records.
Updated operation and maintenance (O&M) manuals.
Up-to-date records support safety, traceability, and regulatory compliance.
Notes: Explain how keeping accurate documentation supports audits and legal defence. Link this to real-world practice and ask learners to explore what documentation exists in their own training or workplace settings.

## Slide 11: Lifecycle cost and sustainability in maintenance
Proactive maintenance lowers whole-life costs
Fewer emergency call-outs and unplanned replacements.
Extends service intervals and defers capital expenditure.
Energy-efficiency preservation
Well-maintained motors, drives and controls run closer to name-plate efficiency.
Prevents wasted energy from worn components or poor lubrication.
Notes: Use real-world cases: onsite PV arrays with neglected cleaning lose output; regular maintenance recovers that yield etc.

## Slide 12: Continued
Asset life extension
Regular servicing of switchgear, transformers and generators delays end-of-life replacements.
Protects return on investment by maximising operational years.
Carbon footprint reduction
Reduced waste and scrap from premature failures.
Lower energy consumption translates to fewer CO₂ emissions.

## Slide 13: Data-driven continuous improvement
Systematic record-keeping
Log every intervention: date, task, findings, actions taken.
Use digital CMMS (Computerised Maintenance Management System) or structured spreadsheets for easy querying.
Trend analysis
Identify repeating faults, seasonal peaks, and emerging degradation.
Prioritise high-frequency failures for deeper root-cause investigation.

## Slide 14: Continued
Risk assessment updates
Feed data back into a risk matrix.
Adjust inspection intervals or techniques based on actual performance.
Closed-loop feedback
Review maintenance KPIs (Key Performance Indicators) quarterly (downtime hours, cost per asset, energy saved).
Continuously refine procedures, update checklists and reallocate resources.

## Slide 15: Summary
You should now be able to:
Identify the two main types of maintenance: planned preventive and reactive
Explain legal responsibilities and industry standards relating to electrical system maintenance
Compare the advantages and limitations of PPM and reactive approaches

## Slide 16
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.