## Slide 1
Occupational Specialism: Electrotechnical Engineering
K1.16 Equipment adjustments as required by installation standards to ensure correct function
PowerPoint 1.16: Equipment adjustments1.16 Equipment adjustments as required by installation standards to ensure correct function
Notes: 643.10
Functional testing
Equipment shall be subjected to functional testing, as appropriate, to verify that it is properly mounted, adjusted and installed and operates correctly in accordance with the relevant requirements of BS 7671. Examples of such equipment are:
﻿﻿switchgear and control gear assemblies, drives, controls and interlocks, ﻿systems for emergency switching off and emergency stopping, insulation monitoring.
NOTE 1: This list is not exhaustive.
Protective devices shall be submitted to a test of their function, as necessary, to check that they are properly installed and adjusted. Where fault protection and/or additional protection is provided by an RCD, the effectiveness of any test facility incorporated in the device shall be verified.
Where an AFDD is installed the effectiveness of any manually operated test facility shall be verified in accordance with the manufacturers' recommendations.
NOTE 2: This functional test does not replace the functional test indicated by the relevant standards.

## Slide 2: Introduction
Give an example of building equipment where adjustable settings are a feature.

## Slide 3: Objectives
By the end of this session, you should be able to:
Explain the purpose of equipment adjustment during commissioning and its link to design intent and safe operation
Demonstrate how to adjust settings in accordance with manufacturer instructions
Document all adjustments clearly in a commissioning certificate or adjustment log

## Slide 4: What is commissioning?
Commissioning is the process of ensuring that a newly installed electrical system or equipment:
operates as intended
complies with design specifications
is safe and efficient before being handed over.
This stage includes testing, inspecting, adjusting and documenting the system’s performance.
Notes: Explain that commissioning goes beyond testing, it ensures final adjustments are made and recorded. It’s the final validation before client use.

## Slide 5: Why are adjustments required?
Electrical devices often include adjustable settings to tailor performance.
Examples include:
time delays on fans or PIRs
current ratings on overload relays
sensitivity of motion detectors.
These must be adjusted according to the designer's intent and in line with the manufacturer's specifications.
Notes: Highlight that default settings are not always suitable. Without proper adjustment, systems may underperform or pose safety risks.

## Slide 6: Common equipment with adjustable settings
Some electrical devices need to be adjusted during commissioning to ensure correct function.
Fan timers, delay time after switch-off.
PIR sensors, lux level, time delay, sensitivity.
Thermostats, temperature set points.
Mechanical ventilation.
These settings must be checked, adjusted if necessary, and recorded as part of the handover process.
Notes: Use props if available. Demonstrate how these settings affect functionality.

## Slide 7: Adjusting fan overrun time
A fan in a bathroom is often wired with a timer module.​
This allows the fan to run for a set time after the light is switched off (e.g. 2–5 mins).​
The setting must be:​
appropriate to the room’s size and use​
set using the dial or DIP switch on the timer module​.
Notes: Explain the importance of balancing effectiveness with energy efficiency and noise concerns.

## Slide 8: Setting thermal overload relays
Thermal overloads are used in motor control circuits.
They protect motors from prolonged overcurrent.
Settings are usually dialled in amps and must match the motor's full load current (FLC).
Check:
motor rating plate
manufacturer data for trip curve
environmental temperature adjustments.

## Slide 9: PIR sensor settings
Passive Infrared (PIR) sensors are adjustable for:
Lux level: Determines ambient light threshold
Time delay: How long light stays on after last movement
Sensitivity: Detection range or radius
Proper adjustment ensures:
energy savings
reduced nuisance switching
longer lamp life.

## Slide 10: Following manufacturer’s instructions
All adjustments must be:
made in accordance with manufacturer guidelines
using correct tools and procedures
avoiding over-tightening, incorrect dials or damage.
Why?
Warranty validity.
Safety.
Compliance with BS 7671.

## Slide 11: Recording and handover
Once adjustments are made:
record them in the commissioning certificate
inform the client or responsible person.
Include any:
user instructions
O&M manuals (Operation and Maintenance)
labels or notices.
Notes: Emphasise that this documentation is essential for future maintenance and inspections.

## Slide 12: Summary
You should now be able to:
Explain the purpose of equipment adjustment during commissioning and its link to design intent and safe operation
Demonstrate how to adjust settings in accordance with manufacturer instructions
Document all adjustments clearly in a commissioning certificate or adjustment log

## Slide 13
Any questions?
Copyright in this document belongs to and is used under licence from the Department for Education, © 2025.
‘T-LEVELS’ and ‘T Level’ are registered trademarks of the Department for Education.
WJEC is authorised by the Department for Education to develop and deliver this T Level Technical Qualification.
WJEC operates in England under the name Eduqas which is a registered trademark of WJEC.